## Slide 1: Comparative scenario Analysis of Mymensingh Town
MSDP Project 2011-2031

## Slide 2: Objectives
Evaluate how the city elements are spatially distributed over the city area (Like landuse, population, resources and facilities)
Evaluated how different area of the city is getting the services & facilities
Identify the exposed area of the city subject to different risk
Evaluate the Connectivity of the city area

## Slide 3: Methodology
City area is divided into 100 m X 100 m grid. Total no of Grid is 2160. each grid size is 1 Hectare.
34 elements are taken as parameter for the analysis
Parameters are examined by two ways:
1. Parameters/elements present within the grid
2. Parameters/elements are connected from the grid center through road network

## Slide 4: Methodology
Depending on element presents in the cell and network distance of the elements from grid center a hierarchy is created so that every cell can be comparable with other.
Spatial Join operation is performed for populating the parameters/elements into the cell
Network Analysis operation is performed for calculating the connectivity/ accessibility of the cell from the elements
A scale is developed ranging 0 to 10. Where each cell is scored according to the distribution.
A weightage factor is assign for each parameter depending on their merit.
Finally all cell are converted into 100 score…

## Slide 5: Weightage distribution of the variables for comparative analysis of the cell in Mymensingh municipality
S/N | item | quality | description | condition of veriable | influance of veriable | Load distribution | Broad category | points | detail points
1 | Pora_dist | point | distance from municipality office | quality outside cell | administrative influance | 50% | 1. Adminstrative | 5 | 2
2 | Upz_Dist | point | distnce from UPZ office | quality outside cell | administrative influance |  |  |  | 1
3 | DCOff_dist | point | distance from DC's office | quality outside cell | administrative influance |  |  |  | 2
4 | PriSch_Dist | point | distance from primary school | quality outside cell | educational influance |  | 2. Education | 6 | 1
5 | Hghsch_dist | point | distance from high school | quality outside cell | educational influance |  |  |  | 2
6 | Col_dist | point | distance from college | quality outside cell | educational influance |  |  |  | 2
7 | Univ_dis | point | distance from college | quality outside cell | educational influance |  |  |  | 1
8 | Clic_Dstn | point | distance from clinic | quality outside cell | health serv. influance |  | 3. Health | 6 | 2
9 | Hos_Dstn | point | distance from hospital | quality outside cell | health serv. influance |  |  |  | 4
10 | CityCent_distn | point | distance from city centre | quality outside cell | commercial influance |  | 4. Commertial | 7 | 5
11 | Bzr_dstn | point | distance from bazar | quality outside cell | commercial influance |  |  |  | 2
12 | Park_distn | point | distance from park | quality outside cell | recreational influance |  | 5. Recreational | 3 | 2
13 | River_distn | line | distance from brahmaputra river | quality outside cell | recreational influance |  |  |  | 1
14 | Lngth_prim | point | distance from primary road | quality outside cell | basic traffic influance |  | 6. Transportationa | 8 | 5
15 | ImpNode_distn | point | distance frim important node | quality outside cell | basic traffic influance |  |  |  | 3
16 | Dhk_bus | point | distance from dhaka bus station | quality outside cell | regional service influance |  | 7. Regional connectivity | 5 | 3
17 | dhk_rail | point | distance from rail station | quality outside cell | regional service influance |  |  |  | 2
18 | PO_dist | point | distance from police station | quality outside cell | basic service influance |  | 8. Distance from Urban services | 10 | 2
19 | Fire_dist | point | distance from fire station | quality outside cell | basic service influance |  |  |  | 3
20 | Dstb_dstn | point | distance from dustbin | quality outside cell | basic service influance |  |  |  | 1
21 | Tel_Dstn | point | distance from telephone post | quality outside cell | basic service influance |  |  |  | 1
22 | Epole_dstn | point | distance from electric post | quality outside cell | basic service influance |  |  |  | 3

## Slide 6: Weightage distribution of the variables for comparetive analysis of the cell in mymensingh municipality
S/N | item | quality | description | condition of veriable | influance of veriable | Load distribution | Broad category | points | detail points
22 | Wat_supply | poly | distance from water line | quality outside cell | direct influance within cell | 50% | 9. quality of direct Urban service | 8 | 2
23 | Drn_line | poly | distance from drain | quality outside cell | direct influance within cell |  |  |  | 2
24 | Rd_Line | poly | distance from nearby road | quality outside cell | direct influance within cell |  |  |  | 1
25 | RD-width | poly | Adjacent road width | quality within cell | direct influance within cell |  |  |  | 3
26 | sum_pop_nt | poly | total population | quality within cell | direct influance within cell |  | 10. Quality of inhabitants | 5 | 5
27 | Sum_built area | poly | total built up area | quality within cell | direct influance within cell |  | 11. Built-up quality | 10 | 4
28 | sum_Build_v | poly | total voulmn of that built up area | quality within cell | direct influance within cell |  |  |  | 6
29 | sum_res_S | poly | total residential area | quality within cell | direct influance within cell |  | 12. Residential | 4 | 4
30 | Sum_admin | poly | total administrative area | quality within cell | direct influance within cell |  | 13. Administrative | 3 | 3
31 | Sum_Othr | poly | total other area | quality within cell | direct influance within cell |  | 14. Others | 5 | 5
32 | sum_edu_sp | poly | total education built area | quality within cell | direct influance within cell |  | 15. Educational | 4 | 4
33 | sum_Mixed | poly | total mixed used area | quality within cell | direct influance within cell |  | 16. Mixed used | 6 | 6
34 | Avg_ht_rl | poly | avarage height (R.L.) | quality within cell | direct influance within cell |  | 17. Physical quality of cell | 5 | 5

## Slide 7: Population Distribution and score of the cell
Chart: Score Against Population
| 1200 | 0
 | 10 | 0

## Slide 8: Building foot print pattern & their score
Chart: Score Against Building Foot Print
| 7500 | 0
 | 10 | 0

## Slide 9: Residential Floor Space distribution and their score
Chart: Score Against Residentail Floor Space
| 15000 | 0
 | 10 | 0

## Slide 10: Commercial, Mixed Floor Space and Ground Height Map

## Slide 11: Accessibility of Each cell connected with Important Node and their score
Chart: Disatnce
| 0 | 250 | 500 | 1000 | 2500 | 5000 | 7500 | 10000
 | 10 | 9 | 8 | 6 | 5 | 2 | 1 | 0

## Slide 12: Accessibility of Each cell connected with Primary School and their score
Chart: Distance
| 0 | 100 | 250 | 500 | 1000 | 2500 | 3000
 | 10 | 9 | 8 | 7 | 5 | 1 | 0

## Slide 13: Comparative scenario of Mymensingh Municipality

## Slide 14
Thank You
Q & A ???